Internet System
Multimedia Networking
P. Bakowski
bako@ieee.org

---
Multimedia networking applications
streaming stored audio and video
streaming live audio and video
real-time interactive audio and video
delay sensitive
loss-tolerant

---
Multimedia networking applications
streaming stored audio and video
stored media
video server rack
streaming
continuous playout

---
Multimedia networking applications
streaming live audio and video
media not stored
multiple streams
     broadcasting

---
Multimedia networking applications
real-time interactive audio and video
no stored media
strong real-time constraints
multicasting

---
Internet evolution
more bandwidth and switching capacity
routing
switching

---
Internet evolution
more bandwidth and switching capacity
content distribution by replication and caching

---
Internet evolution
more bandwidth and switching capacity
content distribution by replication and caching
multicast overlay networks
multicast routers

---
Multimedia protocol stack
RTP and RTCP

---
RTP session types
RTP and RTCP

---
RTP packet

---
RTP packet : payload type
96 to 127 – dynamic (includes H264)

---
RTP packet : timestamp
audio
20 ms * 8000 1/s => 160 (timestamp distance)
reference – media clock audio (8kHz), video (96KHz)

---
RTCP packet

---
RTCP packet: receiver report

---
RTT time computation
NTP – Network Time Protocol – data on 64 bits 0xb44db705 - seconds 0x20000000 - fraction of second

---
Audio capture
analog signal
time

---
Video capture

---
Media frames & packets

---
Packet timing - disruption

---
Packet reception & play-out

---
Play-out buffer

---
Play-out clock skew

---
Play-out time calculation

---
Buffering delay

---
Buffering – network jitter

---
Distribution of network jitter

---
Talk spurts (SN & TS relation)

---
Media frames & Players

---
Operation of media decoder

---
Media multiplexing

---
Multiplexing time-line

---
Receiver lip synchronization

---
Receiver time lines

---
Error cancealement and correction

---
Speach error cancealement (1)

---
Speach error cancealement (2)

---
Error cancealement methods

---
Video codec operation

---
Video motion compensation

---
Packet interleaving

---
Interleaving matrix

---
FEC – parity based error correction

---
FEC – packet repair

---
RTP - FEC packet repair

---
FEC – Redundancy coding

---
RTP - redundancy packet

---
RTP – partial checksum

---
RTCP – transmission feedback

---
Congestion

---
Congestion control with TCP

---
Header compression - principles

---
Header compression - option

---
Compressed (header) RTP packet

---
Summary
Multimedia protocol stack
RTP and RTCP protocols
Audio/video capture
Media frames & packets
Packet reception & play-out
Media synchronization
Error cancealement and repair
Congestion (TCP) and header compression